## Slide 1: Lecture 3
Review of Internet Protocols Transport Layer

## Slide 2: Protocols: HW/SW Interface
Internetworking: allows computers on independent and incompatible networks to communicate reliably and efficiently;
  Enabling technologies: SW standards that allow reliable communications without reliable networks
  Hierarchy of SW layers, giving each layer responsibility for portion of overall communications task, called protocol families or protocol suites
Transmission Control Protocol/Internet Protocol (TCP/IP)
  This protocol family is the basis of the Internet
  IP makes best effort to deliver; TCP guarantees delivery
  TCP/IP used even when communicating locally: NFS uses IP even though communicating across homogeneous LAN
Notes: WS companies used TCP/IP even over LAN
Because early Ethernet controllers were cheap, but not reliable

## Slide 3: Services provided by layers
Each layer in protocol stack provides a “service”
  Uses service from lower layers
Benefits of layering
  Isolates complexity
  Clearly defined interfaces
Protocols implement functionality within layer

## Slide 4
DATA
Application
Pre.
Session
Transport
Network
Data Link
Physical
7
6
5
4
3
2
1
DATA
AH
DATA
PH
DATA
SH
DATA
TH
DATA
NH
DATA
DH
DATA
PH
Application
Pre.
Session
Transport
Network
Data Link
Physical
7
6
5
4
3
2
1
Network
A
B
Layered Network Architecture (OSI)

## Slide 5
TCP/IP Model
ISO OSI (Open Systems Interconnection) not fully implemented
Presentation and Session layers not present in TCP/IP
Application
Pre.
Session
Transport
Network
Data Link
Physical
7
6
5
4
3
2
1
Application
TCP
IP
Host-to-Net
OSI
TCP/IP

## Slide 6: Protocols
Protocols define communication between entities
  Format and order of messages
  Actions taken on transmission and/or receipt of message or other event
Protocols use headers (and trailers) for control information
  Naming depends on layer

## Slide 7: Process-to-process communication
We have a network. How to get between programs?

## Slide 8: Process Communication
How do the end systems communicate?

## Slide 9: Interface-to-interface connectivity
We now have links. How to get across the network?

## Slide 10: Datagrams
Datagrams are forwarded independently

## Slide 11: TCP/IP packet
Application sends message
TCP breaks into 64KB segments, adds 20B header
IP adds 20B header, sends to network
If Ethernet, broken into 1500B packets with headers, trailers
Header, trailers have length field, destination, window number, version, ...
TCP data
(≤ 64KB)
TCP Header
IP Header
IP Data
Ethernet

## Slide 12: Communicating with the Server: The O/S Wall
CPU
User
Kernel
NIC
NIC
PCI Bus
Problems:
O/S overhead to move a packet between network and application level => Protocol Stack (TCP/IP)
  O/S interrupt
  Data copying from kernel space to user space and vice versa
Oh, the PCI Bottleneck!

## Slide 13: The Send/Receive Operation
The application writes the transmit data to the TCP/IP sockets interface for transmission in payload sizes ranging from 4 KB to 64 KB.
The data is copied from the User space to the Kernel space
The OS segments the data into maximum transmission unit (MTU)–size packets, and then adds TCP/IP header information to each packet.
The OS copies the data onto the network interface card (NIC) send queue.
The NIC performs the direct memory access (DMA) transfer of each data packet from the TCP buffer space to the NIC, and interrupts CPU activities to indicate completion of the transfer.

## Slide 14: Transmitting data across the memory bus using a standard NIC
http://www.dell.com/downloads/global/power/1q04-her.pdf

## Slide 15: TCP/IP Processing Path (RX)

## Slide 16: Network I/O Processing
10
100
40
GHz and Gbps
Time
1990
1995
2000
2003
2005
2010
.01
0.1
1
10
100
1000
2006/7
Network bandwidth outpaces Moore’s Law
Moore’s Law
TCP requirements Rule of thumb:
1GHz for 1Gbps

## Slide 17: I/O Acceleration Techniques
Architectural Improvement
TCP Offload: Offload TCP/IP Checksum and Segmentation to Interface hardware or programmable device (Ex. TOEs)
O/S Bypass: User-level software techniques to bypass protocol stack – Zero Copy Protocol
(Needs programmable device in the NIC for direct user level memory access – Virtual to Physical Memory Mapping. Ex. VIA)
All the high bandwidth NICs today employ some kind of TCP Offload and O/S Bypass techniques

## Slide 18: Multiplexing/de-multiplexing
Multiple processes operate on one computer
  Interface address alone is not sufficient to distinguish
Need to (de)multiplex traffic from different processes
5-tuple used for unique identification of connection
  IP source address
  IP destination address
  Transport layer source port
  Transport layer destination port
  Transport layer protocol

## Slide 19
TCP/IP packet
APP. DATA
TCP
IP
MAC
MAC
Source Port
Destination Port
Sequence Number
Acknowledgement Number
Header Length and Options
Window Size
Checksum
Urgent Pointer
Options (0 or more 32-bit words)

## Slide 20
TCP/IP packet
APP. DATA
TCP
IP
MAC
MAC
Ver.
Total Length
Identification
Time to Live
Source Address
IHL
Service Type
Options and Fragment Offset
Protocol
Header Checksum
Options (0 or more 32-bit words)
Destination Address

## Slide 21
TCP/IP packet
APP. DATA
TCP
IP
MAC
MAC
Preamble
D. Add.
S. Add.
CRC
Leng.

## Slide 22: TCP Header: 5-tuple example
5-tuple is reversed for return communication
Destination port is associated with application layer protocol (e.g., 80 for HTTP)
Operating system picks source port randomly

## Slide 23: TCP header
Port numbers
Sequence number
  Position of data
ACK number
  Next expected data
Checksum
Flags for connection setup and teardown

## Slide 24: What functionality does TCP provide?
Reliability
  Recovery from errors in the network layer
Flow control
  Limit transmission rate to not overwhelm receiver
Congestion control
  Limit transmission rate to not overwhelm network

## Slide 25: Reliable data transfer
How can reliability be achieved?
  Consider different assumptions for network layer
Case 1: completely reliable network layer
  Send segment
Case 2: bit errors in network layer
  Add error detection and ACK/NAK
  Add sequence number to handle garbled ACK/NAK
Case 3: bit errors and packet loss in network layer
  Timer to trigger retransmission
  “Stop-and-wait” protocol

## Slide 26: Reliable data transfer
Stop-and-wait has low performance
  How can we increase throughput?
Sliding window
  Allow multiple segments “in-flight”

## Slide 27: Sliding window example

## Slide 28: UDP: bare bones protocol
Ports, length, checksum
  Checksum is optional

## Slide 30: Internet Protocol
IP header
  Source and destination address
  Datagram length
  Upper layer protocol
    Identifies TCP, UDP, etc.
  Time to live
    Protection against accidental loops
  Header checksum
    Protection against bit errors
  Fragmentation possible
    Link layer limited to some datagram size (min. MTU is 576 bytes)

## Slide 31: Other IP aspects
Routing
  Determines forwarding
ICMP
  Error handling
Link layer
  Address resolution (ARP)
  Dynamic IP addresses (DHCP)
Application layer
  Domain names (DNS)
Transport layer
  Network address translation (NAT)
New IP version: IPv6

## Slide 32: Network systems
Data is switched between network stacks

## Slide 33: Classification of network systems
Network system differ by level of protocol processing

## Slide 34: Example network system: NIC
Network interface card / adapter connects to link
Block diagram:

## Slide 35: Example network system: switch
Switch connects multiple links
Block diagram:

## Slide 36: Example network system: switch
System may differ by system architecture
Example: share memory vs. distributed memory

## Slide 37: Application requirements
Different applications have different requirements:

## Slide 38: Throughput preservation
Throughput performance
  Ensure network system can handle link rates at all points
Delay/jitter
  Ensure network system processes traffic quickly
Packet loss
  Ensure sufficient buffer space and fast processing
Most network system design focus on bandwidth

## Slide 39: Packet rate vs. data rate
Data rate states total number of bits per second
Each packet requires specific processing
  Packet rate sometimes more meaningful
What is the packet rate for a 10Gbps link?
  Distinguish small packets and large packets

## Slide 40: System design for throughput
What are the differences between these systems?
  How do they affect throughput preservation?